## Slide 1
Hardware Cache Coherence Analysis in Zynq UltraScale+ MPSoC: CCI-400 Characterization and APU-RPU Communication Performance
Luigi Caucci, Simone Cecere
Department of Electrical Engineering and Information Technology
University of Naples Federico II
Naples, Italy
Email: {l.caucci, simo.cecere}@studenti.unina.it

## Slide 2
System Overview: Zynq UltraScale+ MPSoC Architecture
Heterogeneous Processing Elements
Real-time Processing Unit (RPU):
Dual-core ARM Cortex-R5F @ 533 MHz
32 KB L1 I-cache + 32 KB L1 D-cache per core
No L2 cache subsystem
128 KB Tightly Coupled Memory (TCM)
Deterministic real-time execution
Cache Coherent Interconnect
ARM CoreLink CCI-400:
Up to 5 ACE-compliant slave interfaces
2 ACE-Lite master interfaces to DDR
Snoop Control Unit (SCU) for coherence
AMBA ACE protocol implementation
Base address: 0xFD6E0000
Platform: Kria KR260 Robotics Starter Kit (XCZU5EV variant)
Application Processing Unit:
Quad-core ARM Cortex-A53 @ 1.33 GHz
32 KB L1 I-cache + 32 KB L1 D-cache per core
Shared 1 MB L2 cache (16-way set-associative)
Runs Linux operating system
64-byte cache line granularity

## Slide 3
Motivation and Problem Statement
The Cache Coherence Challenge
Heterogeneous processing elements accessing shared memory require robust cache synchronization to ensure correctness and performance.
Problem: APU writes remain in L2 cache (write-back), while RPU reads stale data from DDR.
Software-managed coherence
Explicit cache flush/invalidate (CP15)
Significant overhead, complex programming
Non-cacheable memory regions
Designate shared memory as non-cacheable
10–100× slower access latency
Hardware-managed coherence
CCI-400 AMBA ACE protocol
Optimal performance Complex multi-layer system configuration

## Slide 4
Zynq UltraScale+ Architecture with CCI-400
CCI-400 Interconnect Architecture
The ARM CoreLink CCI-400 Cache Coherent Interconnect implements the AMBA ACE (AXI Coherency Extensions) protocol with three supplementary channels:
AC (Address Channel Snoop): Interconnect sends snoop requests to masters
CR (Response Channel Snoop): Masters reply with cache line state
CD (Data Channel Snoop): Direct cache-to-cache transfer (bypass DDR)
Key Components
Centralized Snoop Control Unit (SCU)
Hardware performance monitoring counters
Multiple coherence domain configurations
Shareability attribute enforcement

## Slide 5
Cache Incoherence Scenario
Timeline Demonstration of Complete Cache Incoherence
At time t₁, the APU writes a NEW value in L2 cache
Due to write-back policy it’s not propagated immediatly to DDR
At time t₂, the RPU reads directly from DDR and observes the stale OLD value
Absence of hardware cache coherence mechanisms.
Critical Finding: This scenario fundamentally compromises both functional correctness and real-time determinism guarantees in heterogeneous embedded systems.
APU writes NEW
NEW
OLD
NEW
OLD
OLD
OLD
STALE DATA
t0
t1
t2
APU L2
DDR
APU L2
APU L2

## Slide 6
Methodology Overview: Research Approach
Documentation Analysis
Bare-Metal Attempt
Linux with Remoteproc Framework
Userspace Testing via /dev/mem
Kernel Module Development
Performance Characterization

## Slide 7
Documentation Analysis
Identified Documentation Gaps
No integration guide for Linux/Remoteproc with CCI-400
Unclear relationships: PMUFW configuration ↔ FSBL initialization ↔ Device tree
No procedures to verify hardware coherence is actually active
CCI-400 PMU behavior undocumented for Zynq UltraScale+
Kria BSP coherence constraints not explicitly stated
Research Objectives
Systematically characterize CCI-400 behavior and configuration requirements
Develop rigorous experimental methodology for cache coherence verification
Quantify software cache management overhead (nanosecond-resolution)
Enablement & Analysis:
Identify and document prerequisites for CCI-400 activation
Provide theoretical performance analysis with functional hardware coherence

## Slide 8
Remoteproc Framework and Shared Memory Configuration
Device Tree Configuration
reserved-memory {
#address-cells = <2>;
#size-cells = <2>;
ranges;
// Shared memory for APU-RPU experiments (8 MB)
rpu_shmem@3e000000 {
compatible = "shared-dma-pool";
reg = <0x0 0x3e000000 0x0 0x800000>;
no-map;
dma-coherent;
};
};
Base Configuration
openamp.dtb
DTB → DTS
Add Shared Memory Region
DTS → DTB
Shared Memory Organization
Base Address: 0x3E000000 (8 MB total)
Protocol Control Area: 0x3E000000–0x3E3FFFFF (4 MB)
Results Storage Area: 0x3E400000–0x3E7FFFFF (4 MB)

## Slide 9
Kernel Module Design: Definitive Testing Approach
Critical Requirements for Proper Cache Coherence Testing
Producer (APU) - Kernel Module
// Kernel thread running on Cortex-A53
static int writer_thread_fn(void *data) {
while (!kthread_should_stop()) {
// Test Case 1: Write with explicit cache flush
test_buffer[0] = PATTERN_A;
__asm__ __volatile__("dc cvac, %0" :: "r"(&test_buffer[0]));
__asm__ __volatile__("dsb sy" ::: "memory");
msleep(50);
// Test Case 2: Write without cache flush
test_buffer[0] = PATTERN_B;
__asm__ __volatile__("" ::: "memory");
msleep(50);
}
return 0;
}
// Polling loop on Cortex-R5F
while (1) {
// Invalidate cache before reading
Xil_DCacheInvalidateRange((INTPTR)shared_mem, 64);
uint32_t value = shared_mem[0];
if (value == PATTERN_A) {
coherent_reads++;
} else if (value == PATTERN_B) {
incoherent_reads++;
}
}
Consumer (RPU) - Bare-metal Firmware
visible to RPU (flushed to DDR)
retained in APU L1 cache (invisible to RPU)
Should NOT see this - indicates cache problem
Cache flush worked - coherency maintained

## Slide 10
Experimental Results: Definitive Cache Incoherence
Stress Test Results: 100,000 Consecutive Read Operations
Run
Reads
Stale
Fresh
Coherence
1
100,000
100,000
0
0%
2
100,000
100,000
0
0%
3
100,000
100,000
0
0%
Total
300,000
300,000
0
0%
Observation:
RPU reads OLD pattern 300,000/300,000 times
NEW pattern (in APU cache) never detected
Conclusion:❌ CCI-400 hardware coherence is non-functional❌ No snoop operations occurring
Configuration Verification Status
Prerequisite
Status
Layer
Device tree CCI-400 node
✓
OS
dma-coherent property
✓
OS
Shareability attributes
✓
OS
RPU0_CFG COHERENT bit
✓
Register
XPAR_LPD_IS_CACHE_COHERENT
✗
Vivado
PMUFW broadcast enable
✗
Firmware
FSBL snoop port enable
✗
Firmware
Critical Finding: Three missing prerequisites in standard BSP.
Custom firmware modifications are needed.

## Slide 11
Testing Protocol and Stress Test Implementation
Communication Protocol Sequence Diagram
APU
RPU
TTC0
DDR (shared_mem)
read tstart
Write payload, size, tstart, START
Read size, tstart
Wait for START (invalidate cache)
read tend
Write result, ACK
Wait for ACK
Shared Timer Infrastructure
Triple Timer Counter 0 (TTC0):
Base address: 0xFF110000
Clock frequency: ~100 MHz
Time resolution: 10 ns
Counter width: 32-bit
Shared hardware clock eliminates drift
Invalidate metadata
Invalidate payload
Calculate Δt

## Slide 12
Base Overhead Components: Small packets (1–64 bytes, single cache line) exhibit approximately 1.5–1.7 µs baseline overhead comprising:
Polling loop detection latency: ~1.0 µs
Control word and metadata cache invalidation: ~120 ns
Memory barrier instruction execution (DSB): ~50 ns
Protocol state machine overhead: ~300 ns
Large Packet Cache Invalidation Cost: For the maximum 64 KB packet with 1024 cache lines:
Tinvalidation ≈ 1024 × 60 ns = 61.4 µs
Experimentally measured value: 63.4 µs, demonstrating excellent model agreement with prediction error below 3%.
Cache Invalidation Overhead: Scaling Characteristics

## Slide 13
Theoretical Coherent Scenario Performance Model
CCI-400 Hardware Coherence Model
With functional CCI-400:
No explicit software cache invalidation required
Automatic coherence via hardware snoop mechanisms
Eliminates ~60 ns/line software overhead
Result: Direct performance improvement without programmer intervention
Snoop Transaction Latency Breakdown
Base interconnect traversal: ~50 ns
Snoop address broadcast: ~100 ns
Agent responses (3 × 20 ns): ~60 ns
Total round-trip: ~210 ns
Theoretical Transport Time Model
Parameter
Description
Value
Protocol overhead
350 ns
Per-line snoop latency
210 ns
Effective DDR bandwidth
10.5 GB/s

## Slide 14
Size (B)
Non-Coherent (µs)
Coherent (µs)
Speedup
1
1.658
0.310
5.3×
64
1.674
0.315
5.3×
1024
2.588
0.606
4.3×
4096
5.499
0.969
5.7×
16384
17.127
2.107
8.1×
65536
63.443
6.342
10.0×
Geometric Mean:
5.7×
Performance Measurements & Predicted values
Theoretical Coherent Scenario Vs Actual Measurements
Key Performance Characteristics
Measured Performance:
~60 ns per 64-byte cache line
Linear scaling with cache line count
Cost Components:
CP15 DCIMVAC instruction execution
DSB synchronization barrier overhead

## Slide 15
TCM Baseline Characterization
Validating Cache Overhead Isolation
Why TCM Baseline?
Establish architectural lower bound for memory access latency
Validate cache overhead measurements independently
Zero cache involvement → pure hardware timing
Confirm CCI-400 model predictions
Research Objectives
Memory location: 0xFFE00000 (R5F_0 ATCM)
Capacity: 64 KB total (32 KB ATCM + 32 KB BTCM)
Access pattern: APU write-only (consistent with cache overhead measurement)
Timing: Identical TTC0 infrastructure @ 100 MHz
Protocol: Same APU-RPU communication structure
Measurement Methodology
: Before metadata/command writes
: After write completion (no RPU wait)

## Slide 16
TCM vs DDR: Comparison Plot
Comparative Results
Latency
Capacity
Coherency
Use Case
TCM
0.61 μs
64 KB
N/A
<1KB real-time
DDR (no-CCI)
3.50 μs
4 GB
Software
Current baseline
DDR (w/CCI)
0.51 μs*
4 GB
Hardware
Target
*Predicted from validated model
Key Findings
Cache overhead isolated: 3.50 - 0.61 = 2.89 μs
5.7× penalty from software cache management
Model validation: TCM (0.61 μs) ≈ CCI pred. (0.51 μs)
60 ns/line confirmed: 2.89 μs ÷ 48 lines ≈ 60 ns
Critical Insight TCM proves sub-μs is achievable WITHOUT cache overhead, validating our CCI-400 speedup predictions

## Slide 17
TCM and CCI-400: Complementary Solutions
Requirements:
Computer vision: Multi-MB image buffers exceed TCM
Neural networks: Weight tensors (MBs) cannot fit
Sensor fusion: Aggregate data streams too large
Ideal for ultra-small (<1KB) real-time control loops
TCM Role:
Proves cache overhead is dominant factor
Validates theoretical CCI-400 model
Confirms sub-μs latency achievable
Cannot replace CCI for general-purpose use
Criterion
TCM
DDR + CCI
Latency
0.61 μs
0.51 μs (pred.)
Capacity
64 KB
4 GB
Scalability
Fixed 64KB
Expandable
APU access
0.61 μs
0.51 μs
Use cases
Tiny buffers
All workloads

## Slide 18
Conclusions: Principal Findings
Coherence Verification
100,000 iterations: 100% stale data reads
Proof: CCI-400 hardware coherence is disabled
Software Overhead Quantification
Cache invalidation: ~60 ns per 64-byte cache line
Scales linearly with cache line count
CCI-400 Potential Performance
Predicted speedup: 4–10× improvement
Average: 6× faster across packet sizes
Critical Missing Prerequisites
Critical Conclusion:
CCI-400 requires complete custom Vivado project from scratch
This negates the value proposition of using pre-integrated commercial platforms
XPAR_LPD_IS_CACHE_COHERENT Macro
Requires custom Vivado hardware design
Not available in standard Kria BSP
PMUFW Broadcast Enable
Platform Management Unit must configure IPI controller
Enables RPU snoop request propagation through CCI-400
FSBL Snoop Port Configuration
First Stage Bootloader (EL3 privilege) must program CCI-400 registers
Enable hardware snooping on slave port S2 (RPU interface)

## Slide 19
Limitations and Future Work
Limitations and Assumptions
Polling Overhead: Measured latencies include ~1 μs RPU polling variability (interrupt-based mechanisms would reduce this)
Single RPU Core Utilization: Experimental measurements utilize one R5F processor core. Activating both RPU cores would double coherence-related snoop traffic
Synthetic Communication Pattern: Regular periodic packet transmission does not comprehensively represent all possible inter-processor communication patterns
Future Research Directions
Custom Vivado Design: Develop hardware satisfying all CCI-400 prerequisites for experimental validation
Interrupt Mechanisms: Replace polling with mailbox interrupts to reduce latency and improve power efficiency
Multi-Core Analysis: Test both RPU cores simultaneously to study snoop contention and arbitration
Representative Workloads: Evaluate performance with real applications (ADAS sensor fusion, industrial control)

## Slide 20
Thank you for your attention!
Luigi Caucci M63001679
Simone Cecere M63001681
Università degli studi di Napoli Federico II